## Slide 1: End-to-end architecture
NDOVU HAULAGE LTD | FLEET RISK COMMAND CENTRE
1
Operational Data Sources
Vehicle maintenance logs
Fuel transactions
GPS / telematics
Trips and deliveries
Vehicle register
2
Databricks: Data Engineering
Bronze: raw data
Silver: cleaned data
Gold: business-ready tables
3
SQL Risk Detection Engine
Rules and scores calculated from data
Maintenance risk
Abnormal fuel consumption
Dispatch risk
Delivery delays
4A
Power BI
Executive dashboard, fleet KPIs, trends, and high-risk vehicles
4B
n8n
Reads new or unresolved risk records and orchestrates alerts
5
Gemini AI
Explains the detected risk using the supplied evidence and drafts suggested next steps
6
Automated Email Alert
Risk
Evidence
Potential impact
Recommended investigation
7
Human Decision and Follow-up
Fleet manager investigates, maintenance team responds, dispatcher checks clearance, and the outcome is recorded
Rules detect.
AI explains.
People decide.
Notes: End-to-end flow: operational data lands in Databricks (Bronze, Silver, Gold). A SQL engine turns Gold tables into four risk types. Power BI shows the picture; n8n reads new or unresolved risk records, asks Gemini to explain each one from the supplied evidence, and sends an email. People decide and the outcome is recorded.

## Slide 2: Ndovu sees its trucks every 10 minutes and still finds the problem after the loss
THE PROBLEM IN ONE SENTENCE
Breakdowns and fuel are managed by generic service intervals and month-end invoices. The signals that could prevent the loss already exist in telematics, fuel cards, the TMS and the workshop, but they sit in four portals that nobody joins and nobody interprets in time.
Ndovu Haulage Ltd is a fictional Kenyan haulier used as the case study.
40
trucks
48
drivers
8
corridors
3,241
trips in one quarter
Notes: Set the scene: a 40-truck fleet, 48 drivers, 8 corridors. The data exists, but it is not joined or interpreted in time.

## Slide 3: Eight corridors, one fleet, and no shared picture of its health
WHERE NDOVU OPERATES
Mombasa
Nairobi
Malaba
Kisumu
Eldoret
Nakuru
Garissa
Taveta
Namanga
Schematic, not to scale
Route | Distance
Mombasa - Nairobi | 485 km
Nairobi - Malaba | 500 km
Nairobi - Garissa | 370 km
Nairobi - Kisumu | 345 km
Mombasa - Taveta | 330 km
Nairobi - Eldoret | 310 km
Nairobi - Namanga | 165 km
Nairobi - Nakuru | 160 km
Cargo: containers, perishables, general freight, fuel and chemicals, construction. Late delivery is penalised by the hour.
Notes: Trucks run the Northern Corridor and regional routes. Perishables and containers carry SLA penalties by the hour, so every delay has a price.

## Slide 4: An emergency breakdown costs about five times a planned service, before penalties
CRISIS 1 | UNPLANNED HIGHWAY BREAKDOWNS
Average cost per work order (USD)
Chart: 
| Planned service | Emergency breakdown
Avg cost USD | 708 | 3632
16
breakdowns in a quarter, each stranding a load for 19 hours on average
$217,833
SLA penalties paid in the quarter
3 to 5x
roadside repair versus scheduled workshop servicing
Why it happens
"Service every 10,000 km" ignores coolant creep, falling oil pressure, a hot gearbox and worn brake linings.
Notes: Figures come from the Ndovu demo dataset (one quarter, 40 trucks). Emergency repairs include parts, labour and recovery. The SLA penalty total covers all late trips.

## Slide 5: Fuel leaves the tank weeks before the invoice tells anyone
CRISIS 2 | FUEL ANOMALIES AND PHANTOM SIPHONING
Day 0
Truck fuels and runs the trip
Days 7 to 25
Station invoice finally arrives
Day 30+
Month closes, theft is "found"
Fuel is 30% to 50% of operating cost for East African haulage companies, so a few percent of leakage is a large number.
Four ways fuel leaks
Siphoning at roadside stops or depots
Long idling in port and border queues
Fuel-card transactions larger than what reached the tank
Poorly calibrated engines burning more per 100 km
What the tank sensors reveal in the demo data
110
siphon events, 9,767 L, found by 5 drivers
125
fuel-card transactions billed for more fuel than the tank received
$28,959
leaked in one quarter by a 40-truck fleet
Notes: Without sensor reconciliation, none of this is visible until invoices land and the month is closed. Figures are from the demo dataset where theft patterns were planted for testing.

## Slide 6: Dispatch cannot see what telematics and the workshop already know
CRISIS 3 | THE GAP BETWEEN DASHBOARDS AND OPERATIONS
Telematics portal
Fault code P0218: transmission over-temperature on KBZ 123A
?
Workshop notes
"Gearbox noise reported" in a notebook, not synced
?
Dispatch desk
Assigns KBZ 123A a 485 km Mombasa - Nairobi run
101
trips were dispatched while the truck had an open Critical or High fault code
across 13 trucks in one quarter. The data was in the portal. Nobody acted on it in time.
Notes: The dashboard exists, but it is a portal people have to remember to open. The dispatcher assigns trips from the TMS, which knows nothing about open fault codes.

## Slide 7: Alerts nobody can interpret become a clear brief the fleet manager can act on
WHERE AI FITS | GEMINI
TODAY: A RAW ALERT
KBZ 123A
DTC P0218 | sev HIGH
TRANS_TEMP_MAX_24H 123
TRANS_TREND +21
HEALTH 32 | P48H 0.84
IMPACT_USD 8404
Accurate, but it needs an expert to read it, and it arrives with no owner and no next step.
Gemini
NEXT: THE EMAIL THE FLEET MANAGER RECEIVES
Risk
Transmission fault developing on KBZ 123A, with a high chance of breakdown within 48 hours.
Evidence
Open code P0218, gearbox temperature up 21 C versus the prior 48 hours, health score 32 of 100, 84% breakdown probability.
Potential impact
About $8,404 in emergency repair and SLA penalties if it fails on the road.
Recommended investigation
Hold dispatch. Check gearbox oil level and temperature, scan the transmission controller, inspect the clutch, then confirm clearance.
Illustrative output. Gemini receives only rule-generated evidence, and a person verifies before acting.
Notes: Gemini is the explanation layer. It receives only the evidence the SQL rules produced and drafts a plain-language brief with next steps. If Gemini is unavailable, a rule-based email still goes out.

## Slide 8: What the Fleet Risk Command Centre must change
OBJECTIVES AND TARGET KPIs
Objective | KPI | Target
Cut unplanned breakdowns | Breakdowns per 1,000 trips | -50% in 6 months
Cut SLA penalties | SLA penalties, USD per month | -40%
Stop dispatch of faulty trucks | Dispatches with an open Critical or High fault | Zero Critical, under 2% High
Shift repairs to planned work | Emergency share of maintenance cost | Under 20%
Reduce fuel leakage | Siphoning, over-billing and excess burn as % of fuel spend | Under 1%
Detect fuel theft fast | Time from event to alert | Under 1 hour (today about 3 weeks)
Faster, consistent investigation | Alert to recorded decision | Under 4 hours for Critical
Close the loop | Alerts with a recorded outcome | Over 95%
Notes: Targets are design goals for the programme, to be validated against the baseline once real data is connected.

## Slide 9: Rules detect, AI explains, people decide
SCOPE AND GUARDRAILS
Rules detect
Transparent SQL scores and thresholds find maintenance, fuel, dispatch and delay risk. Every alert can be audited.
AI explains
Gemini turns the supplied evidence into a plain-language brief and drafts next steps. It cannot lock trucks or change data.
People decide
Fleet manager investigates, maintenance responds, dispatcher checks clearance, and the outcome is recorded.
In scope
Telemetry, fault codes, trips, fuel cards, workshop data
Health scoring and 48-hour failure risk
Fuel, dispatch and delivery-delay rules
Gemini email briefs with human follow-up
Power BI command centre
Out of scope
Tyre management, route optimisation, driver behaviour beyond idling

## Slide 10: Every risk explained, owned and closed before the truck leaves the yard
WHAT SUCCESS LOOKS LIKE
0
Critical-fault dispatches
<4 h
From alert to recorded decision
95%+
Alerts with a recorded outcome
Built on Databricks, SQL risk rules, Power BI, n8n and Gemini.